## Slide 2
DESIGNING & BUILDING WOODFRAME STRUCTURES with INEXPENSIVE MATERIALS
By Brooks Stover, MMR

## Slide 3
Describe how I
DESIGN and BUILD
wood framed structures
without breaking the bank!
CLINIC OBJECTIVE

## Slide 4
January 1979…
‘been doing this a long time!
…June and July 2008

## Slide 5
It had lots of wood structures with CHARACTER!
Modeling the BUFFALO CREEK & GAULEY
for 30+ years

## Slide 6
Many
Very Simple Wood-Framed Structures
Railbus Shed
Tool Storage Shed

## Slide 7
Company Store at Swandale
Dairy at Cressmont
Others structures were larger…but still wood and still full of character

## Slide 8
I needed to learn how to model them
…quickly and easily!

## Slide 9
DESIGN
A. THREE basic “FORM Elements”
B. SIX basic “TEXTURE Elements”
CONSTRUCTION
C. Inexpensive MATERIALS
D. CONSTRUCTION Step by Step
OUTLINE

## Slide 10
DESIGN
A. THREE basic “FORM Elements”
B. SIX basic “TEXTURE Elements”
CONSTRUCTION
C. Inexpensive MATERIALS
D. CONSTRUCTION Step by Step
OUTLINE

## Slide 11
PITCHED Roof
FLAT Roof
SHED Roof
A. “FORM” ELEMENTS
Most wood –frame structures can be built from combinations of one or more of these
3 BASIC FORMS

## Slide 12
Combine 3 Basic FORMS to Create All Kinds of Structures…
…by Varying Sizes & Proportions

## Slide 13
45+ Structures on My BC&G Layout Use Just These
THREE Basic FORMS!

## Slide 14
The 40 Structures on My BC&G Layout Use
Just These
THREE Basic Forms!
Most interesting structures use a combination of the 3 forms...

## Slide 15
I enjoy finding the three forms in the structures others build…

## Slide 16
And in real structures…

## Slide 17
PITCHED Roof
FLAT Roof
SHED Roof
Learn to build these 3 basic forms and you can build almost any wood-frame structure!
And there’s really little difference between these 3!

## Slide 18
Only 2 structures on my layout have “intersecting roofs”
J.G. Bradley’s House
Dundon Shop’s Office

## Slide 19
DESIGN
A. THREE BASIC “FORM Elements”
B. SIX BASIC “TEXTURE Elements”
CONSTRUCTION
C. Inexpensive MATERIALS
D. CONSTRUCTION Step by Step
OUTLINE

## Slide 20
Lap Siding
Exposed Rafters
Tar Paper
Board & Batten
Roof Fascia Boards
Shingles
B. SIX “TEXTURE” ELEMENTS
Wall Construction
Roof Construction
Roofing Material
“Add Visual Variety to the 3 Form Elements”

## Slide 21
TEXTURE ELEMENT – “Wall Construction”
Lap Siding
(Horizontal)
Board & Batten
(vertical)

## Slide 22
TEXTURE ELEMENTS – “Roofing Material”
Tar Paper
Shingles

## Slide 23
TEXTURE ELEMENTS – “Roof Construction”
Exposed Rafters
(‘rough’)
Roof Fascia Boards
(‘smooth’)

## Slide 24
Incorporating a variety of TEXTURES on a structure adds visual interest

## Slide 25
DESIGN
A. THREE BASIC “FORM Elements”
B. SIX BASIC “TEXTURE Elements”
CONSTRUCTION
C. Inexpensive MATERIALS
D. CONSTRUCTION Step by Step
OUTLINE

## Slide 26
C. MATERIALS
Inexpensive
Easy to Cut and Glue
Easy to Paint
Durable
“Old Fashioned” Paper and Wood
“Old Fashioned” Tape and Glue

## Slide 27
“Old Fashioned” Paper and Wood
Standard Balsa and
Bass Stripwood
1/16” Mat Board
“3 x 5” Cards

## Slide 28
Adhesives
“Old Fashioned” Tape and Glue
“Duco” Cement
3M Adhesive Transfer Tape
“Blue Painter’s Tape”

## Slide 29
DESIGN
A. THREE BASIC “FORM Elements”
B. SIX BASIC “TEXTURE Elements”
CONSTRUCTION
C. Inexpensive MATERIALS
D. CONSTRUCTION Step by Step
OUTLINE

## Slide 30
D. CONSTRUCTION
Simple Office with 2 FORMS and all 6 TEXTURES
- Lap Siding - Batten Siding
- Shingles - Tarpaper
- Fascia Boards - Exposed Rafters

## Slide 31
1. Lay out walls directly on Mat Board
Cut window and door openings to fit castings
Avoid centering windows or doors on walls for added interest

## Slide 32
Cut out walls can be taped loosely together and placed on layout to confirm size, etc.
Roofs painted black

## Slide 33
2. Apply adhesive transfer tape to back of cards
3. Cut card stock in to strips about 1/4 “ wide
Making Lap Siding

## Slide 34
4. Start at foundation line and apply ‘peel and stick’ strips, overlapping to obtain desired ‘board size’.
Interior wall of adjoining form
Cover window openings

## Slide 35
Cutting and applying siding irregularly creates look of aging building. Painted paper looks naturally weathered.

## Slide 36
5. Turn wall over, trim edges and cut out windows

## Slide 37
6. Applying Battens
- Use strip wood for battens
- Leave clearance for window frames
- Trim after gluing
* Batten construction even on larger buildings
* Making own batten siding allows flexibility in spacing
Making Batten Siding

## Slide 38
7 - 8. Install Corner ‘Braces” and Reinforce walls
a. Use 1/4” square balsa for corner joints
b. Reinforce large walls with additional 1/4” square balsa
* Fits at joints are not critical

## Slide 39
9 -10. Assemble walls together
This…
NOT this…
c. Be sure side walls fit INSIDE end walls
* Use gluing fixture to assure square corners

## Slide 40
Interior walls use same basic techniques
Corner reinforcement
Square wood bracing
Mat board interior walls
* Windows made from micro-tape

## Slide 41
Scratchbuilding Windows
Chart Pak brand micro Tape
1
2
3

## Slide 42
11. Final Assembly and Trim
Prepaint then install corner trim
Install windows

## Slide 43
12-13. Roof and Roof Trim
a. Glue triangular pieces cut in first step to form roof
b. Add fascia board using strip wood
c. Apply roofing material and ridge beam of 1/16” square balsa

## Slide 44
14 - 15. Roof and Roof Trim (con’t)
d. Make exposed rafters from small pieces of strip wood, typically 1/16 x 1/8” on scale 16” centers.

## Slide 45
16-17. Roof Details & Porches
Add commercial roof details. Corrugated material makes great ‘patches’. Make porch roof from mat board with strip wood posts.

## Slide 46
The FINISHED PRODUCT!

## Slide 47
Cressmont Dairy

## Slide 48
Widen Machine Shops

## Slide 49
Sullivan Manufacturing
Model Railroader May 2013

## Slide 50
Dundon Company Store & Feed Storage Building

## Slide 51
Board by Board
Abandoned Mine

## Slide 52
Clement’s Mining Company
MODEL RAILROADER Oct. 2014

## Slide 53
Rich Run Mine

## Slide 54
THREE BASIC “FORM Elements”
- Shed, Pitched and Flat Roof
B. SIX BASIC “TEXTURE Elements”
- Lap Siding and Board & Batten
- Shingles and Tar Paper
- Exposed Rafters and Fascia Trim
C. “Old Fashioned” Paper Materials
SUMMARY
Most wood-frame structures can be built from just THREE BASIC FORMS.
Visual variety and interest can be added by varying the SIDING construction, ROOFING materials and EAVE details
PAPER products and WOOD are inexpensive yet make durable models.
There’s great satisfaction from having a structure you built yourself on your layout!

## Slide 55
Clinic Handout

## Slide 56
OPEN DISCUSSION

## Slide 57
OPEN HOUSE
Friday 6 – 11 pm
Sunday Noon to 5 pm
Trick or Treat Snacks Available!

## Slide 59
END

## Slide 60
Model
Photography
Scratchbuilding
Structures
Operating
Scheme
Modeling Philosophy
Prototype Information
Complete Layout
Tour
Rolling Stock & Structures
126 Pages, Full Color, Soft Cover
“MODELING THE BC&G”

## Slide 61
2. Apply adhesive transfer tape to back of cards
3. Cut card stock in to strips about 1/4 “ wide
Scrap paper
5 x 7 “ card
Making Lap Siding

## Slide 62
4. Start at foundation line and apply ‘peel and stick’ strips, overlapping to obtain desired ‘board size’. Exaggerate ‘joints’.
“foundation”

## Slide 63
5. Turn wall over, trim edges and cut out windows